## Slide 1: CS 771 Presentation
Classifying Heart Sounds Challenge
By: Group 12
Atulya Shivam Shree
Rajesh Shubhankar
Richa Sharma
Rishabh Nigam

## Slide 2: Challenge
Heart beat data – using
Clinical Trial – dataset B
IPhone app – dataset A
Challenge1 – Segmentation of heart data to find S1 and S2 peaks.
Challenge2 – Classification of heart sound into normal, murmur, extra heart sound and Artifact for dataset A and normal, murmur, extrasystole for dataset B.

## Slide 3: Dataset
Dataset available in .wav and .aif format. We use data from .wav format.
Dataset A contains data at 44100 frames per second, Dataset B at 4000 frames per second
Training File: segmentation data is provided in a csv for 21 and 90 files for dataset A and B respectively

## Slide 4: Challenge1 : Step1 decimation
Decimate the signal by a factor of 20 for dataset A and for 2 for dataset B. This brings down the frequency close to 2000 for both the datasets.
Normalize the signal to (-1,1)

## Slide 5: Challenge1: Step2 Shannon Energy
S

## Slide 6: Challenge1: Step3 smoothening
We use “triangular smooth” to smoothen the signal

## Slide 7: Complete preprocessing

## Slide 8: Challenge1: Step4a getPeaks
We use a threshold and extract all values above the threshold. Then we select the best peak among the neighbouring peaks within a range.

## Slide 9: Algorithm: getS1Peaks

## Slide 10: Algorithm: getS1Peaks

## Slide 11: Challenge1: Step4b getS1Peaks
In this we start with the assumption the S1peaks have higher energy. We start by picking the peak with the maximum energy. Then we look at peaks within distance of one time period of it, and so on. We vary the time period and pick the best set of S1Peaks.

## Slide 12: Challenge1: Step4c getS2Peaks
Look between 2 S1 peaks, and pick the best peak. If no peak is found we lower the threshold and look again.

## Slide 13: Challenge1: Step4d FixPeaks
Fix peaks uses the length of diastolic and systolic period to fix which is S1 and S2.

## Slide 14: Result comparison

## Slide 15: Result comparison

## Slide 16: Challenge2: AttributeSet
We use 14 attributes to classify heart data.
best_frequency;
Systolic_period;
Diastolic_period;
Diastolic_period_variance;
Systolic_period_variance;
number_of_peaks_after_findmaxpeak;
number_of_peaks_finally;

## Slide 17: Challenge2: AttributeSet
S1Peaks_Energy;
S2Peaks_Energy;
Extra_Peaks_Energy;
systolicPeriodEnergy
diastolicPeriodEnergy
time_period_variance
ratio_threshhold_peaks_to_final_peaks

## Slide 18: Challenge2: Results dataset1

## Slide 19: Challenge2: Results dataset1

## Slide 20: Challenge2: Results dataset1

## Slide 21: Challenge2: Results dataset1

## Slide 22: Challenge2: Results dataset2

## Slide 23: Challenge2: Results dataset2

## Slide 24: Challenge2: Results dataset2

## Slide 25: Challenge2: SummaryResults

## Slide 26: Challenge2: SummaryResults

## Slide 27: Results using 5 fold validations: Support Vector Machine
Dataset B
Correctly Classified Instances 69.2308 %
Incorrectly Classified Instances 30.7692 %
Mean absolute error 0.3177
Root mean squared error 0.4117
Relative absolute error 90.8775 %
Root relative squared error 98.6397 %
Total Number of Instances 312
Dataset A
Correctly Classified Instances 54.8387 %
Incorrectly Classified Instances 45.1613 %
Mean absolute error 0.3051
Root mean squared error 0.3894
Relative absolute error 82.9609 %
Root relative squared error 90.8359 %
Total Number of Instances 124

## Slide 28: Results using 5 fold validations: Neural Networks
Dataset B
Correctly Classified Instances 64.7436 %
Incorrectly Classified Instances 35.2564 %
Mean absolute error 0.2705
Root mean squared error 0.4267
Relative absolute error 77.3767 %
Root relative squared error 102.232 %
Total Number of Instances 312
Dataset A
Correctly Classified Instances 54.8387 %
Incorrectly Classified Instances 45.1613 %
Mean absolute error 0.2406
Root mean squared error 0.4187
Relative absolute error 65.4115 %
Root relative squared error 97.6673 %
Total Number of Instances 124

## Slide 29: References
Heart Sound Segmentation Algorithm Based on Heart Sound Envelolgram .H Liang, S Lukkarinen, I Hartimo .Helsinki University of Technology, Espoo, Finland.
Sapire DW. Understanding and diagnosing paediatric heart disease: Heart sounds and murmurs. Norwalk, Connecticut, Applcton & Langc 1992: 27-43.
A Robust Heart Sound Segmentation and Classification Algorithm using Wavelet Decomposition and Spectrogram. Yiqi Deng , Peter J Bentley. Dept. of Computer Science, UCL Malet Place, London.
Classifying heart sounds using peak location for segmentation and feature construction. Emanuel Pereira,Elsa Ferreira Gomes. Institute of Engineering (ISEP/IPP) Porto,Portugal

## Slide 30: Code
Will be available at http://github.com/rishabhnigam31/heartSegmentation.git
Thank You